## Slide 1
    OSE Facilities Directors Conference
    Hickory Knob State Park
    October 21, 2021
    Deferred Maintenance & Alterations using the IEBC
    OSE Project Manager
    Clint Burdett

## Slide 2
IEBC
    See OSE Table 3E, What is your project?
      Alteration
      Addition
      Change of Occupancy

## Slide 3
OSE Table 3E

## Slide 4
Alteration
    Any CONSTRUCTION or RENOVATION TO AN EXISTING STRUCTURE
Addition
    An EXTENSION or INCREASE in floor area, number of stories, or height of a building.
Change of Occupancy
    A change in the USE of a building or portion of a building that results in any of the following.
      Change of Occupancy Classification
      Change from one group to another within an occupancy classification

## Slide 5
After choosing which project type you then choose which Compliance Method:
  Prescriptive
  Work area
  Performance
  You can not mix and match methods, you must pick a method and follow the code requirements of that method

## Slide 6
Option 1: Prescriptive Compliance Method Chapter 5 IEBC
    This method requires that alterations shall comply with the requirements of the IBC for new construction.
    The alteration shall not make the building less complying than the building was prior to the alteration.

## Slide 7
Option 1: Prescriptive Compliance Method Chapter 5 IEBC
    Fire Resistance Ratings. Where applicable, this method allows for the reduction in fire resistance ratings of building elements with the addition of a fire sprinkler system.
    Exceptions
      Stairways and handrail extensions in stairways.

## Slide 8
Proposed corridor extension

## Slide 9
Option 2: Work Area Compliance Method Chapters 6-12 IEBC
    This method is based on a proportional approach to compliance where upgrades are triggered by the type and extent of the work. There are three levels of work.
      Alteration level 1
      Alteration level 2
      Alteration level 3

## Slide 10
Alteration level 1 chpt 7
Alteration level 3 chpt 7-9
Alteration level 2 chpt 7 & 8
Option 2 work area compliance method

## Slide 11
Alteration level 1
  Level 1 Alterations include the REMOVAL and REPLACEMENT or covering of existing materials, elements, equipment, or fixtures using new materials for the same purpose.
    Level 1 alterations shall comply with chapter 7 of the IEBC.
    In level 1 alterations an existing building shall not be altered such that the building becomes less safe than its existing condition.

## Slide 12
Alteration level 1 chpt 7
Alteration level 3 chpt 7-9
Alteration level 2 chpt 7 & 8
Option 2 work area compliance method

## Slide 13
Alteration level 2
  Level 2 Alterations include the RECONFIGURATION of space, the addition or elimination of any door or window, the reconfiguration or extension of any system or the installation of any additional equipment.
    Level 2 alterations shall comply with chapter 7 & 8 of the IEBC.

## Slide 14
Alteration level 1 chpt 7
Alteration level 3 chpt 7-9
Alteration level 2 chpt 7 & 8
Option 2 work area compliance method

## Slide 15
Alteration level 3
  Level 3 Alterations include the RECONFIGURATION of space where the work area exceeds 50% of the building area.
  Level 3 alterations shall comply with chapter 7, 8 & 9 of the IEBC.

## Slide 16
Option 3: Performance Compliance Method Chapter 13 IEBC
    This section is based on an evaluation process that includes a numerical scoring system involving various safety issues and the degree of code compliance for each issue.
    A performance code requires that the building as a whole performs to a certain standard.

## Slide 17
Additions Chapters 11 IEBC
    An addition is an extension or increase in the floor area, number of stories, or height of a building.
    An addition to a building shall comply with the IBC for new construction.
    The main question is the attached wall.

## Slide 18
Change of Occupancy Chapters 10 IEBC
    A change in the use of a building. A change of occupancy shall include a change of occupancy classification or a change from one group to another within the same classification.
    An alteration that includes a Change of Occupancy must be brought up to meet the code requirements of the IBC for the new occupancy.

## Slide 19
Historic Buildings Chapters 12 IEBC
    They must go thru a process with the State Historic Preservation Office (SHPO).
    The agency and A/E should prepare a plan of action for the treatment of historic properties using one of the following:
      Preservation
      Rehabilitation
      Restoration
      Reconstruction

## Slide 20
Accessibility for Existing Buildings section 305.
    A facility that is altered shall comply with the IBC unless technically infeasible.

## Slide 21
Alterations on a Primary Function
    Accessibility is required if alterations are on a primary function.
    Exceptions
      Alterations not on a primary function
      Not exceed 20% of the costs.
      Windows, hardware, controls, electrical, mechanical, fire protection alterations only do not require accessibility requirements.
      Entrances not on a primary function

## Slide 22
Toilet Rooms
    Toilet rooms on a primary function shall be accessible unless technically infeasible.
      If technically infeasible then an accessible family or assisted use toilet is permitted in accordance with IBC.

## Slide 24
What is wrong with this picture?

## Slide 25
What is wrong with this picture?

## Slide 26
What is wrong with this picture?

## Slide 27
What is wrong with this picture?

## Slide 28
What is wrong with this picture?

## Slide 29
Interesting urinal

## Slide 30
Interesting signage